ON THE STABILITY OF SEMI-ACTIVE CONTROL

WITH SEQUENTIAL DRY FRICTION

Tudor SIRETEANU*, Marius Giuclea**, Emanuele GUGLIELMINO***

*Institute of Solid Mechanics of the Romanian Academy, 15 Constantin Mille St., 70701, Bucharest, Romania,

**National Institute of Microtechnology, Computational Intelligence Lab., P.O. Box 38-160, 72225, Bucharest, Romania,

***University of Bath, Department of  Mechanical Engineering,  Bath,  BA2 7 AY, U.K.

Corresponding author: Tudor SIRETEANU, E-mail: siret@mecsol.ro

This paper presents the stability properties obtained for semi-active control strategy of the vehicle suspensions. The classical case is studied by direct Lyapunov method and it is shown that the closed-loop system is asymptotically stable, even for a more general class of damping forces, which includes sequential dry friction. It is also analyzed the stability of fuzzy controllers derived from the semi-active balance logic. In this case it is proved that the developed control systems are globally stable on the bases of stability indexes method.

Keywords: Semi-active control, Stability, Lyapunov function, Fuzzy control system

# INTRODUCTION

In the area of vibration isolation the number of works that highlight the advantages of semi-active control has increased in the last years, [6]-[10]. Most of the papers published on this topic studied the performances of the proposed semi-active control strategies for vehicle suspensions, machinery foundations or earthquake protection systems. The semi-active control with dry friction of the ground vehicles suspensions assures better vibration isolation properties than the passive damping, both for deterministic and random excitations, [9]. In addition, the fuzzy control approach derived from the semi-active paradigm of balance logic leads to a reduction of the chattering effect for the same performance index values, [8], [10].

In this paper the classical and the fuzzy controllers of semi-active suspension with dry friction are studied from the stability point of view. Using reasoning based on Lyapunov function, in the crisp case, it is proven the asymptotic stability of the closed-loop control system. For the fuzzy controllers developed in [8] and [10], is also given a proof for the global stability of control system.

__________________________

Recommended by Radu P.VOINEA

Member of the Romanian Academy

This result is based on the theory of stability indices proposed in [1] and [4].

The paper contains three main sections. The first part consists in the proof of the stability of the classical semi-active control. In the next section the stability indices used for fuzzy case are presented. The third section shows the global stability (both for the single and two degree of freedom vehicle suspension models). The final section includes some general remarks on the methods used in this paper for the stability property proofs.

1. STABILITY OF SDOF MODEL

In this section the stability of a SDOF model of a vehicle suspension with semi-active control is studied.

The proof of stability property is given for a general class of damping forces that includes the sequential dry friction damping.

Consider the system described by:

|  | (1) |
| --- | --- |

where Fd is supposed to be a generic nonlinear controlled damping force of the type:

with ,

subject to the switching law:

.

The previous relations can be written as:

|  | (2) |
| --- | --- |

The vehicle suspension with semi-active dry friction is obtained if  and .

Using the relation (2), equation (1) has the following form:

|  | (1’) |
| --- | --- |

By introducing the state variables  and , the equation (1’) is equivalent to:

|  | (3) |
| --- | --- |
|  | (4) |

Consider the Lyapunov function associated with the first order differential equations (3), (4):

From the definition it follows directly that V is continuous and positive definite function. The proof of the stability property is based on the following theorem (Barbashin-Krasowsky):

If (negative semidefinite) and if the set of the points of the state space for which  does not include any complete trajectory (except the origin), then the system is asymptotically stable.

The first derivative of V is:

|  | (5) |
| --- | --- |

Using the conditions  it is obvious from (5) that  and the set of points for which  is . Next, according to the previous theorem, in order to prove the asymptotic stability, it is sufficient to show that the trajectories of the system (3), (4) are not contained within the abscissa axis. This can be readily verified considering the tangent vector to the trajectory for . Its components are , hence it is orthogonal to the abscissa axis. Therefore the hypotheses of stability theorem are fulfilled and the equilibrium (0,0) is asymptotically stable.

2. STABILITY INDICES FOR DYNAMICAL SYSTEMS

In this section are shortly presented some results on the stability indices that are useful for studying stability properties of fuzzy control systems [1], [4]. Consider the control system given by:

|  | (6) |
| --- | --- |

where (X(Rn, (U(Rm, x=(x1, x2, …, xn)T.

In case of a linguistic fuzzy control system, the control signal is a map

|  | (7) |
| --- | --- |

with .

2.1Two dimensional case

For  the equations (6) and (7) become:

|  | (8) |
| --- | --- |
|  | (9) |

Next, is supposed that the following conditions hold: ; ,  are monotonous functions and the equilibrium position

O(0,0) is stable.

The simplest ways such that the system given by (8), (9) become unstable are static bifurcation and Hopf bifurcation. In order to analyze these two cases is considered the Jacobian matrix of the control system at O(0, 0):

and characteristic polynomial of J:

|  | (10) |
| --- | --- |

where , and  is the trace of the matrix J.

It is known that  leads to a saddle bifurcation and  to a Hopf bifurcation Consequently, a measure of the relative stability in origin is given by the following two indices: . The larger the positive values of  and  are, the greater will be the degree of relative stability of the control system at origin. If one of these indices becomes zero then the system losses the stability property.

Next is pointed out a measure of how far is the system from the appearing of new attractors out of the origin. This situation is possible to take place only in the subspace defined by:

|  | (11) |
| --- | --- |

If  is the solution of (11), , and are the abscissas of the points of  S which are closest to the origin then  . Let us denote

|  | (12) |
| --- | --- |

As one can see, the positive value of  assures the global stability of control system if the local stability property holds. It is important to notice that for two-dimensional case the positive values of the indices ,  and  are both necessary and sufficient conditions for the origin global stability.

2.2 The general case

Let J be the Jacobian matrix of control system at the origin. The associated characteristic polynomial is

|  | (13) |
| --- | --- |

with . The static bifurcation is described by. For Hopf bifurcation  is written in the form:

.

A necessary condition for this type of bifurcation is . Therefore:

- if  the condition is reduced to so ;

- if  is obtained  and then ;

Consequently, if , >0 then the origin is a stable equilibrium of the control system (,  are local indices). For studying the global stability, the index  is determined as in two-dimensional case.

4. STABILITY OF SEMI-ACTIVE SUSPENSION WITH FUZZY CONTROLLER

In this section is studied the stability of fuzzy controllers for semi-active suspensions derived from the semiactive paradigm of balance logic, as in [8] and [10].

For the case of single degree of freedom (SDOF) suspension system the fuzzy control system described in [8] is considered. The mathematical model of the SDOF semi-active suspension is:

where m is the sprung mass,  the relative displacement, kx the elastic force,  the excitation induced by the road profile and 2( is a dimensionless parameter which scales the friction force magnitude. In a dimensionless form the model equations become:

|  | (14) |
| --- | --- |

If  is fuzzy controller output, then the closed-loop control system has the form:

|  | (15) |
| --- | --- |

In order to test the stability using stability indices the following notations are used:

In the matrix notation the control system without forcing term is modeled by

|  | (16) |
| --- | --- |

The fuzzy controller with output  is described by:

- fuzzy partitions as in the figure 1: a) for inputs  and ; b) for output  ;

- rule base presented in table 1;

- inference procedure - “simplified reasoning method”, see [11];

After some calculations is obtained  as follows:

where a and b are scaling coefficients associated to x1 and x2, respectively. It is easily seen that

which implies that the Jacobian matrix at origin is J = A.. Therefore  and .

Consequently, the closed-loop control system is stable at the origin. In addition, and , so the subspace for the index  is an empty set and therefore the control system has no other equilibrium point except the origin.

Finally, according to the stability indices method, the equilibrium O(0, 0) is globally stable for the considered control system.

a)

b)

Fig. 1 - Fuzzy partitions of variable domains for SDOF case

Table 1 Fuzzy rule base for SDOF case

| y'F yF | N | Z | P |
| --- | --- | --- | --- |
| N | Z | M | B |
| Z | Z | Z | Z |
| P | B | M | Z |

In the case of two degree of freedom (2DOF) semi-active suspension system, the quarter-car model used in [10] is described by:

where  M is a quarter of the body mass, m - mass of the wheel with semiaxis,  - absolute displacement of vehicle body,  - absolute displacement of the wheel center,  - stiffness coefficients of the suspension and tire, respectively,  - the suspension damping coefficient and u - the output of fuzzy controller.

Using the notations: ,              and:

then the system can be written in the form (16).

The characteristic equation of the free system is:

|  | (17) |
| --- | --- |

with

The corresponding Hurwitz matrix will be:

Next is tested the Routh-Hurwitz criterion:

.

Therefore all eigenvalues of A have negative real part (A is stable).

The main elements of fuzzy controller consist in, [10]:

- input vector

and normalized input Y0 given by  with a, b positive constants; so

- fuzzy partitions of variables domains (denoted by Y1, Y2 for inputs and U for output) depicted in figure 2;

- fuzzy rule base presented in table 2:

- inference procedure - “simplified reasoning method”;

Fig. 2 - Fuzzy partitions of variables domains in 2DOF case

Table 2 Fuzzy rule base for 2DOF case

| y20 y10 | NB | NM | NS | Z | PS | PM | PB |
| --- | --- | --- | --- | --- | --- | --- | --- |
| NB | Z | Z | Z | Z | B | B | B |
| NM | Z | Z | Z | Z | M | M | M |
| NS | Z | Z | Z | Z | S | S | S |
| Z | Z | Z | Z | Z | Z | Z | Z |
| PS | S | S | S | Z | Z | Z | Z |
| PM | M | M | M | Z | Z | Z | Z |
| PB | B | B | B | Z | Z | Z | Z |

For a fuzzy rule of type (Ai, Bi, Ci fuzzy sets on Y1, Y2 and U respectively):

Ri: If y10 is Ai and y20 is Bi then u0 is Ci

with i=1, 2, …, 49 the firing of antecedents will be computed with the fuzzy intersection “product”:

.

If  is the abscissa of the set Ci and taking into account the equidistant partitions of domains (), then the fuzzy output is computed as follows:

Finally the expression of  can be represented graphically as in figure 3.

Fig. 3 - The value of fuzzy control signal u0

Therefore, if then

.

Finally, is obtained

As in the SDOF case  for i=1,.., 4, and therefore J = A. The local stability indices have the following values:

and

.

Again  so the subspace for  is empty. Finally is inferred the conclusion that  is a globally stable equilibrium of the system.

4. CONCLUSIONS

This paper contains an analysis of the stability properties of the semi-active control with sequential dry friction, both for crisp and fuzzy cases derived from the semi-active paradigm of balance logic. In the first situation, the asymptotic stability is proven for a larger class of damping forces that includes as a particular case the sequential dry friction. For the sake of simplicity this study is performed on a SDOF vehicle model, but the proof can be given in the same way for the general case. In the fuzzy case are considered two fuzzy control systems involved in SDOF and 2DOF suspension models. On the basis of stability indices method is shown that both control systems have the global stability property of the corresponding equilibrium points.

As a consequence, one can conclude that semi-active control strategy leads to a stable closed-loop control system, both in classical and fuzzy case.

ACKNOWLEDGEMENT

The authors wish to express their gratitude to the Romanian Academy and Royal Society for their financial support, which has made this collaborative programme possible.

REFERENCES

- ARACIL, J., OLLERO, A., GARCIA-CEREZO, A., Stability Indices for the Global Analysis of Expert Control Systems, IEEE Transaction on Systems, Man and Cybernetics, 19, no. 5, pp. 998-1007, 1999.

- DRIANKOV, D., HELLENDORN, H., REINFRANK, M., An Introduction to Fuzzy Control, Berlin, Heidelberg, Springer Verlag, 1993.

- GIUCLEA, M., NEGOITA, M., A GA Method to Optimize the Design Parameters of the Fuzzy Systems, Second International ICSC Symposium on Fuzzy Logic ISFL’97, Zurich, pp. 171-175, 1997.

- ARACIL, J., OLLERO, A., GARCIA-CEREZO, A., Robust design of rule-based fuzzy controllers, Fuzzy Sets and Systems, no. 70, pp. 249-273, 1995.

- PARK, D., KANDEL, A., LANGHOLTZ, G., Genetic-Based New Fuzzy Reasoning Models with Application to Fuzzy Control, IEEE Transaction on Systems, Man and Cybernetics, 1, pp. 39-46, 1994.

- SIRETEANU, T., BALAS, C., Forced vibrations of sequentially damped oscillator, Simpozionul anual al Institutului de Mecanica Solidelor, Bucharest, pp. 1-6, 1992.

- SIRETEANU, T., The effect of sequential damping on ride comfort improvement, I. Mech. E. C., 145, Vehicle Noise and Vibration, pp. 77-82, 1984.

- SIRETEANU, T., STAMMERS, C. W., GIUCLEA, M., URSU, I., GUGLIELMINO, E., Semi-active suspension with fuzzy controller optimized by genetic algorithm, International Conference on Noise and Vibration Engineering, ISMA 25, Leuven, Proceedings CD-ROM, 2000.

- STAMMERS, C. W., SIRETEANU, T., Vibration control of machines by use of semi-active dry friction damping, Journal of Sound and Vibration, 209, no.4, pp. 671-684, 1998.

- URSU, I., URSU, F., SIRETEANU, T., STAMMERS, C.W., Artificial intelligence based synthesis of semiactive suspension systems, The Shock and Vibration Digest, 32, no. 1, January 2000, Sage Science Press Publications, Inc., Thousand Oaks*London*New Delhi.

- YAGER, R., R., FILEV, D., P., Essentials of Fuzzy Modeling and Control, John Wiley & Sons, 1994.

### Receives March 26, 2002

# Text boxes

1

0

0.5

1

Z

M

B

0

0.5

0.5

N

Z

P

1

0

1/3

-1/3

NS

Z

PS

1

2/3

1

PM

PB

-2/3

-1

NM

NB

Y1, Y2

1

0

1/3

1

Z

M

B

S

2/3

U

u0=1

u0=3y20

u0=0

u0=0

u0=-y10

u0=-3y10y20

u0=0

u0=0

u0=0

u0=0

u0=0

u0=0

1/3

-1/3

u0=-3y10y20

u0=y10

u0=1

u0=-3y20

1

-1

y20

y10